Some facts about film flatness:

Horizontal and vertical profile lines of the film surface in a roll film 120 magazine. Second frame after a waiting time of 5 minutes. Negative values mean, that the film surface is closer to the lens.

Horizontal and vertical profile lines of the film surface in a roll film 120 magazine. Second frame after a waiting time of 30 minutes. Negative values mean, that the film surface is closer to the lens. The strong deviation at the left side is caused by the memory effect of the film bending on the roller before the frame window.

Topographic map of film surface in a roll film 120 magazine, camera with vertical transportation direction. Colour coded height levels are in (m.  Shown “film flatness” situation  is valid for the second frame after a waiting time of 30 minutes.

Topographic map of film surface in a roll film 120 magazine, camera with horizontal transportation direction. Colour coded height levels are (m.  Shown “film flatness” situation  is valid for the second frame after a waiting time of 30 minutes.

Through-focus MTF curves at f/5.6, they illustrate how effective MTF on film is affected by above described topographic structure of film surface.